General Description

Technical grade calcium chloride is produced with special attention to quality and consistency.  Our ISO system ensures that our high standards are maintained and improved.

Applications

Technical grade calcium chloride is used in a multitude of applications within a wide variety of industries.  It is used:-

- In water purification to precipitate fluorides, sulphates and phosphates

- As an agent to remove moisture in domestic and industrial applications.

- As an additive in concrete to decrease setting time, especially in cold weather conditions

- In the oil industry to provide high density clear brine fluids.

- In the pulp and paper industry to improve printability.

- For alginate production as a thickening agent.

- As an emulsion breaking agent in latex and plastic production.

Availability

Solid technical grade calcium chloride flakes are produced in Finland.  Solid technical grade calcium chloride is available in the following packaging options.

| SOLID TECHNICAL GRADE cAcL2 PACKAGING |
| --- |
| Package | Dimensions LxWxH | Units |
| 25 kg bag | 1080x1070x1050 | 42/pallet |
| 1000 kg big bag | 1000x1000x1350 | 1 |
| Bulk | N/A | N/A |

**Also available in 500kg bags on requeste**

Safety and Handling

Calcium chloride is a strong salt.  Protective clothing, rubber gloves and eye protection are recommended.  Rubber safety boots should also be worn in work areas, since calcium chloride can damage leather.  This product should be handled in areas with proper ventilation.  Before using this product, refer to the MSDS (available from Peacock Salt) for complete safety and handling guidelines.  For proper disposal guidelines for calcium chloride wastes, consult the appropriate local regulatory authorities.

Calcium chloride is a hygroscopic product and should be stored indoors on pallets at normal temperatures.  If stored according to recommendations, the maximum shelf life is two (2) years.

Physical Properties

Appearance					White flakes

Odour						None

Bulk density					800 to 900 kg/m³

Chemical Properties

|  | Specification | Typical Value |
| --- | --- | --- |
| CaCl2 Concentration | > 77% | 78% |
| Residual mass as H2O | N/A | 18-22% |
| pH (in 10% CaCl2 solution @ 20°C) | 9 – 11 | 10.4 |
| Na | < 1% | 0.7% |
| Alkalinity as Ca(OH) 2 | < 0.3% | 0.1% |
| Insoluble in water | < 0.20% | 0.05% |
| Mg | < 200 mg/kg | 60 mg/kg |
| SO4 | < N/A | < 0.01% |
| Fe | < 5 mg/kg | 1 mg/kg |

Typical Sieve Analysis

| Sieve | Approximate % passing |
| --- | --- |
| 6.3 mm | 100 |
| 4 mm | 90 |
| 2 mm | 30 |
| 1 mm | 10 |